567—81.3 (455B) Wastewater treatment plant grades.

81.3(1) Classifications. The wastewater treatment plant classifications are listed in the following table:

Wastewater Treatment Plant Classifications

| Treatment Type | Grade |
| --- | --- |
|  | Based on Design Pounds of BOD5/day |
|  | less than 334 | 334-835 | 836-2,505 | 2,506-8,350 | more than 8,350 |
|  | Based on Design Population Equivalent |
|  | less than 2,000 | 2,000-5,000 | 5,001- 15,000 | 15,001- 50,000 | more than 50,000 |
| 1. Primary Treatment | I | I | II | III | IV |
| 2. Waste Stabilization Lagoon | IL | IL | IL | IL | IL |
| 3. Aerated Lagoon System | IL | IL | IIL | IIL | IIL |
| 4. Fixed Film Biological Treatment | II | II | III | III | IV |
| 5. Activated Sludge | II | III | III | IV | IV |

81.3(2) Unknown design BOD  5  loading. When the design BOD 5  loading is unknown, the plant BOD 5  loading shall be determined by using the average pounds of BOD 5  of the 24-hour composite samples taken in the last 12 months. If no 24-hour composite samples were taken, then grab samples shall be used.

81.3(3) IL and IIL wastewater operator requirements. A Grade I, II, III, or IV wastewater treatment certificate will satisfy the certification requirements for a Grade IL plant. A Grade II, III, or IV wastewater treatment certificate will satisfy the certification requirements for a Grade IIL plant.