321.258  Arrangement of lights on official traffic-control signals.

1.  Colored lights placed on a vertical official traffic-control signal face shall be arranged from the top to the bottom in the following order when used:

a.  Circular red.

b.  Steady or flashing left-turn red arrow.

c.  Steady or flashing right-turn red arrow.

d.  Circular yellow.

e.  Circular green.

f.  Straight-through green arrow.

g.  Steady left-turn yellow arrow.

h.  Flashing left-turn yellow arrow.

i.  Left-turn green arrow.

j.  Steady right-turn yellow arrow.

k.  Flashing right-turn yellow arrow.

l.  Right-turn green arrow.

2.  Colored lights placed on a horizontal official traffic-control signal face shall be arranged from the left to the right in the following order when used:

a.  Circular red.

b.  Steady or flashing left-turn red arrow.

c.  Steady or flashing right-turn red arrow.

d.  Circular yellow.

e.  Steady left-turn yellow arrow.

f.  Flashing left-turn yellow arrow.

g.  Left-turn green arrow.

h.  Circular green.

i.  Straight-through green arrow.

j.  Steady right-turn yellow arrow.

k.  Flashing right-turn yellow arrow.

l.  Right-turn green arrow.

[C79, 81, §321.258]

2014 Acts, ch 1026, §77; 2014 Acts, ch 1123, §17; 2020 Acts, ch 1063, §147, 148

Subsection 1, paragraphs b and c amended

Subsection 2, paragraphs b and c amended