761—511.11 (321,321E) Single-trip permits. Single-trip permits are issued for indivisible vehicles or indivisible loads for travel when either the dimensions or the weight or both the dimensions and the weight exceed statutory limits. The permit shall be for a specific route between an origin and destination. Single-trip permits are issued for the following:

511.11(1) Vehicles with indivisible loads, including construction machinery, mobile homes and factory-built structures, provided the following are not exceeded:

a.   	 Width. 14 feet 0 inches.

b.   	 Length. 80 feet 0 inches overall.

c.   	 Height. Limited only to the height of underpasses, bridges, power lines, and other established height restrictions. The carrier shall be required to contact affected public utilities when the height of the vehicle with load exceeds 16 feet 0 inches. At the discretion of the permit-issuing authority, a written verification may be required from the affected utility.

d.   	 Weight. See rule 511.12(321,321E).

e.   	 Distance. Unlimited distance over specified routes.

511.11(2) Rescinded IAB 4/28/93, effective 6/2/93.

511.11(3) Vehicles with indivisible loads, including construction machinery, mobile homes and factory-built structures, provided the following are not exceeded:

a.   	 Width. 40 feet 0 inches overall.

b.   	 Length. 120 feet 0 inches overall.

c.   	 Height. Limited only to the height of underpasses, bridges, power lines, and other established height restrictions. The carrier shall be required to contact affected public utilities when the height of the vehicle with load exceeds 16 feet 0 inches. At the discretion of the permit-issuing authority, a written verification may be required from the affected utility.

d.   	 Weight. See rule 511.12(321,321E).

e.   	 Distance. Limited at the discretion of the permit-issuing authority. The following factors shall be considered:

Road conditions; road width; traffic volume; weather conditions; and roadside obstructions, including bridges, signs and overhead obstructions.

511.11(4) Vehicles especially designed for the movement of grain bins and vehicles with indivisible loads, including construction machinery, mobile homes and factory-built structures, provided the following are not exceeded:

a.   	 Width. Must comply with Iowa Code section 321.454.

b.   	 Length. 120 feet 0 inches overall.

c.   	 Height. Statutory: 13 feet 6 inches.

d.   	 Weight. See rule 511.12(321,321E).

e.   	 Distance. Unlimited distance over specified routes.

511.11(5) Vehicles with divisible loads of hay, straw or stover provided the following are not exceeded:

a.   	 Width. 12 feet 5 inches.

b.   	 Length. Must comply with Iowa Code section 321.457.

c.   	 Height. Statutory: 13 feet 6 inches.

d.   	 Weight. See rule 511.12(321,321E).

e.   	 Distance. Unlimited.

This rule is intended to implement Iowa Code sections 321.454, 321.456, 321.457, 321.463, 321E.1, 321E.2, 321E.9, 321E.28 and 321E.29.