761—511.7 (321,321E) Annual permits. Annual permits are issued for indivisible vehicles or indivisible loads for travel when the dimensions of the vehicle or load exceed statutory limits but the weight is within statutory limits. Routing is subject to embargoed bridges and roads and posted speed limits. Annual permits are issued for the following:

511.7(1) Vehicles with indivisible loads, including construction machinery, mobile homes and factory-built structures, provided the following are not exceeded:

a.   	 Width. 12 feet 5 inches including appurtenances.

b.   	 Length. 120 feet 0 inches overall.

c.   	 Height. 13 feet 10 inches.

d.   	 Weight. See rule 511.12(321,321E).

e.   	 Distance. Movement is allowed for unlimited distance; routing through the office of motor carrier services is not required.

511.7(2) Vehicles with indivisible loads, including construction machinery, mobile homes and factory-built structures, provided the following are not exceeded:

a.   	 Width. 14 feet 6 inches.

b.   	 Length. 120 feet 0 inches overall.

c.   	 Height. 15 feet 5 inches.

d.   	 Weight. See rule 511.12(321,321E).

e.   	 Distance. Movement is restricted to 50 miles unless trip routes are obtained from the office of motor carrier services or the route continues on at least four-lane roads. Trip routes are valid for five days.

511.7(3) Vehicles with indivisible loads, including construction machinery, mobile homes and factory-built structures, provided the following are not exceeded:

a.   	 Width. 16 feet 0 inches.

b.   	 Length. 120 feet 0 inches.

c.   	 Height. 15 feet 5 inches.

d.   	 Weight. See rule 761—511.12(321,321E).

e.   	 Distance. Trip routes must be obtained from the office of motor carrier services.

511.7(4) Rescinded IAB 1/23/02, effective 2/27/02.

511.7(5) Truck trailers manufactured or assembled in the state of Iowa provided the following are met:

a.   	 Width. Not to exceed 10 feet 0 inches.

b.   	 Length. Overall combination length must comply with Iowa Code section 321.457.

c.   	 Height. Statutory: Not to exceed 13 feet 6 inches.

d.   	 Weight. See rule 511.12(321,321E).

e.   	 Speed. Rescinded IAB 2/7/01, effective 3/14/01.

f.   	 Roadway width. At least 24 feet 0 inches.

g.   	 Limited movement. Movement shall be solely for the purpose of delivery or transfer from the point of manufacture or assembly to another point of manufacture or assembly within the state or to a point outside the state and shall be on the most direct route necessary for the movement.

511.7(6) Vehicles with divisible loads of hay, straw or stover provided the following are not exceeded:

a.   	 Width. 12 feet 5 inches.

b.   	 Length. Must comply with Iowa Code section 321.457.

c.   	 Height. Statutory: 13 feet 6 inches.

d.   	 Weight. See rule 511.12(321,321E).

e.   	 Distance. Unlimited.

This rule is intended to implement Iowa Code sections 321.454, 321.456, 321.457, 321.463, 321E.1, 321E.2, 321E.10, 321E.28, 321E.29 and 321E.29A and Iowa Code Supplement section 321E.8 as amended by 2002 Iowa Acts, Senate File 2192, section 36.