661—265.25(100) Fireworks site plan review and approval.

265.25(1) Plan approval.

a. 	A license is required for each location where the retail sales of consumer fireworks are conducted. The plan(s) for each retail sales location, including any permanent or temporary building or structure, and for each building or structure used for the storage of fireworks must be submitted.

b. 	Every location where the retail sales of consumer fireworks take place or where consumer fireworks are stored, including any permanent or temporary building(s) or structure(s), must do so in accordance with NFPA 1124.

c. 	The retailer or community group shall also submit to the state fire marshal’s office the proposed plan(s), including any required site plan(s) for the location(s) and for any building(s) or structure(s), whether permanent or temporary, that will be used for the storage of fireworks.

d. 	The plan(s) will be reviewed to determine whether it is in accordance with NFPA 1124. If the plan(s) is incomplete or noncompliant, the retailer or community group will receive notification of deficiencies that need to be corrected.

Note: Regarding the incorporation of the reference to NFPA 102, 1995 edition, Standard for Grandstands, Folding and Telescopic Seating, Tents, and Membrane Structures into NFPA 1124 concerning tents and membrane structures, Sections 7.3.5 and 7.4.8.1.2 of NFPA 1124 should be read together with Section A.7.4.8.1.2 in the Explanatory Material in Annex A to NFPA 1124 and used for the purposes of (1) determining the requirements for the means of egress in tents and membrane structures except as modified by Section 7.3.14 of NFPA 1124 for special requirements for the retail sales of consumer fireworks, and (2) to prohibit the use, discharge, or ignition of fireworks within the tent or membrane structure. The other provisions of NFPA 1124, including the sections relating to the retail sales of consumer fireworks in tents or membrane structures, remain applicable.

265.25(2) Plans not required. In the discretion of the state fire marshal, plans may not be required in the following circumstances:

a. 	For permanent buildings or temporary structures in which only exempt amounts of first-class or second-class consumer fireworks are offered for sale, pursuant to section 7.3.1, NFPA 1124. The licensee shall make current product inventory information available to the state fire marshal upon request.

b. 	For permanent buildings that were licensed in the previous year and for which there have been no changes to the site, building or floor plan. If any changes have been made, a new or updated plan shall be submitted.

c. 	For permanent buildings which are currently classified as a retail occupancy and in which second-class consumer fireworks are the only fireworks are offered for sale.

[ARC 3124C, IAB 6/21/17, effective 5/31/17; ARC 3592C, IAB 1/17/18, effective 2/21/18]