567—49.6(455B) Location of wells. Wells shall be located with consideration given to the lot size, contour, porosity and absorbency of the soil, local groundwater conditions, flooding, and other factors necessary to implement the rules. The lack of specific distances to other possible sources of contamination, such as refuse disposal sites and high-pressure gas lines, does not minimize their potential hazard. These must be evaluated in each particular situation and a distance arrived at that is based on pertinent facts. The well contractor shall consult the administrative authority for assistance in determining a proper distance in such cases.

49.6(1) Minimum distances. The following minimum lateral distances from all private wells shall apply for the common structures or sources of contamination listed in the following table.

Table 49.6(1) Minimum Lateral Distances, Private Wells

| Structure or Source of Contamination | Minimum Lateral Distance (feet) |
| --- | --- |
|  | Shallow Well1 | Deep Well1 |
| Public water supply well | 400 | 200 |
| Formed manure storage structure, confinement building, feedlot solids settling facility, open feedlot | 200 | 100 |
| Transmission pipelines (including, but not limited to, fertilizer, liquid petroleum, or anhydrous ammonia) if a more restrictive setback is not set by the pipeline owner | 200 | 100 |
|  | All Private Wells |
| Earthen manure storage basin, runoff control basins and anaerobic lagoons (see subrule 49.6(2) below) | 1000 |
| Drainage wells | 1000 |
| Solid waste landfills and disposal sites2 | 1000 |
| Domestic wastewater lagoon | 400 |
| Preparation or storage area for spray materials, commercial fertilizers or chemicals that may result in groundwater contamination | 150 |
| Existing wells that do not conform to this chapter | 100 |
| Liquid hydrocarbon storage tanks, except for liquid propane gas (LPG) | 100 |
| Private sewage disposal systems – open portion of treatment system3 | 100 |
| Private sewage disposal systems – closed portion of treatment system3 | 50 |
| Flowing streams or other surface water bodies | 25 |
| LPG storage tanks | 15 |
| Roadside ditch and road rights-of-way | 15 |
| Existing wells that conform to this chapter | 10 |
| Sewer of cast iron with leaded or mechanical joints, sewer of plastic pipe with glued or compression joints, independent clear water drains, cisterns, well pits, or pump house floor drains | 10 |
| Yard hydrants | 10 |
| Frost pit | 10 |
| Property lines (unless a mutual easement is signed and recorded by both parties) | 4 |

1“Deep well” and “shallow well” are defined in 567—49.2(455B).

2Solid waste means garbage, refuse, rubbish, and other similar discarded solid or semisolid materials, including but not limited to such materials resulting from industrial, commercial, agricultural, and domestic activities.

3Private sewage disposal system is defined in 567—subrule 69.1(2). Open portions of treatment systems include subsurface absorption systems, mound systems, intermittent sand filters, constructed wetlands, open bottom media filters, and waste stabilization ponds. Closed portions of treatment systems include septic tanks, aerobic treatment units, fully contained media filters, and impervious vault toilets. These separation distances also apply to septic systems that are not considered privately owned.

49.6(2) Exception to minimum lateral distances. The minimum separation distance between a well and an anaerobic lagoon, earthen manure slurry storage basin, earthen manure storage basin, or runoff control basin shall be 400 feet if the lagoon or basin was permitted by the department after January 1, 1989, or if the applicant demonstrates through percolation testing that the seepage loss through the lagoon or basin does not exceed 1/16 inch per day (0.0625 inch/day). The percolation test shall meet the requirements of ASTM-1587 and 567—subrule 65.15(11).

49.6(3) Frost pits. Wells are not permitted to be located within frost pits. Frost pits that do not contain wells are permitted for the purpose of housing pressure tanks and valves, for example, provided the frost pits are not located closer than ten feet from any well.

49.6(4) Relation to buildings. The well shall be located so that no building interferes with reasonable access for cleaning, treatment, repair, testing, inspection and other maintenance. Wells shall not be located in basements.

49.6(5) Easements. No well shall be located on a property not owned by the well owner unless an easement allowing such placement is reviewed and approved by the administrative authority and the easement is legally recorded.

[ARC 6190C, IAB 2/9/22, effective 3/16/22]