567—81.3(455B) Wastewater treatment plant grades.

81.3(1) Classifications. The wastewater treatment plant classifications are listed in the following table:

Wastewater Treatment Plant Classifications

| Treatment Type | Grade |
| --- | --- |
|  | Based on Design Pounds of BOD5/day |
|  | less than 334 | 334-835 | 836-2,505 | 2,506-8,350 | more than 8,350 |
|  | Based on Design Population Equivalent |
|  | less than 2,000 | 2,000-5,000 | 5,001- 15,000 | 15,001- 50,000 | more than 50,000 |
| 1. Onsite Treatment System | W | Not Applicable | Not Applicable | Not Applicable | Not Applicable |
| 2. Waste Stabilization Lagoon System | IL | IL | IL | IL | IL |
| 3. Aerated Lagoon System | IL | IL | I | I | I |
| 4. Advanced Aerated Lagoon System | II | II | II | II | II |
| 5. Fixed Film Biological Treatment System | II | II | III | III | IV |
| 6. Activated Sludge System | II | III | III | IV | IV |

81.3(2) Unknown design BOD5 loading. When the design BOD5 loading is unknown, the plant BOD5 loading shall be determined by using the average pounds of BOD5 of the 24-hour composite influent samples taken in the last 12 months. If 24-hour composite influent samples are not available, then grab samples shall be used.

81.3(3) IL wastewater operator requirements. A Grade I, II, III, or IV wastewater treatment certificate will satisfy the certification requirements for a Grade IL plant.

81.3(4) Grade W onsite wastewater classification. Any wastewater treatment plant that discharges to a water of the state and that utilizes onsite wastewater treatment technologies, such as those specified in 567—Chapter 69, but excluding waste stabilization ponds, shall be classified as an onsite treatment system (Grade W).

[ARC 6193C, IAB 2/9/22, effective 3/16/22]