567—119.5 (455D,455B) Tanks.

119.5(1) Aboveground. In addition to the requirements imposed by the office of the state fire marshal, the following standards are applicable to aboveground waste oil collection tanks:

a.   	 The tank shall be of sufficient size to handle the projected quantities of used oil to be returned to this specific collection site.

b.   	 The tank shall be designed and maintained to prevent the spillage or discharge of waste oil. Tanks must be set upon an impermeable surface engineered to contain potential spills.

c.   	 Absorbent material shall be available at the tank site for use by the operator to control waste oil spillage or discharge.

d.   	 The tank shall have a level gauge or some other adequate means for checking the oil level within the tank.

e.   	 The tank shall be constructed in accordance with American Petroleum Institute specifications and standards.

119.5(2) Underground. Underground storage tanks used to collect or store waste oil shall comply with the standards in part 8 of division IV of Iowa Code chapter 455B, entitled “Underground Storage Tanks,” and the promulgated rules, Iowa Administrative Code, 567—Chapters 135 and 136.