761—511.9(321,321E) All-systems permits. All-systems permits are issued by the vehicle and motor carrier services bureau for indivisible vehicles or indivisible loads for travel on the primary road system and specified city streets and county roads when the dimensions of the vehicle or load exceed statutory limits but the weight is within statutory limits. Routing is subject to embargoed bridges and roads and posted speed limits. The vehicle and motor carrier services bureau will provide a list of the authorized city streets and county roads. Permit holders shall consult with local officials when traveling on county roads or city streets for bridge embargo, vertical clearance, detour, and road construction information. These permits are issued for the following:

511.9(1) Vehicles with indivisible loads, including special mobile equipment, mobile homes and factory-built structures, provided the following are not exceeded:

a. 	Width. 12 feet 5 inches including appurtenances.

b. 	Length. 120 feet 0 inches overall.

c. 	Height. 13 feet 10 inches.

d. 	Weight. See rule 761—511.14(321,321E).

e. 	Distance. Movement is allowed for unlimited distance; routing through the vehicle and motor carrier services bureau and city and county jurisdictions is not required.

511.9(2) Vehicles with indivisible loads, including special mobile equipment, mobile homes and factory-built structures, provided the following are not exceeded:

a. 	Width. 14 feet 6 inches.

b. 	Length. 120 feet 0 inches overall.

c. 	Height. 15 feet 5 inches.

d. 	Weight. See rule 761—511.14(321,321E).

e. 	Distance. Movement is restricted to 50 miles unless trip routes are obtained from the vehicle and motor carrier services bureau and city and county jurisdictions or the route continues on at least four-lane roads. Trip routes are valid for five days.

511.9(3) Vehicles with indivisible loads, including special mobile equipment, mobile homes and factory-built structures, provided the following are not exceeded:

a. 	Width. 16 feet 0 inches.

b. 	Length. 120 feet 0 inches.

c. 	Height. 15 feet 5 inches.

d. 	Weight. See rule 761—511.14(321,321E).

e. 	Distance. Trip routes must be obtained from the vehicle and motor carrier services bureau and city and county jurisdictions.

511.9(4) Rescinded IAB 1/23/02, effective 2/27/02.

511.9(5) Truck trailers manufactured or assembled in the state of Iowa provided the following are met:

a. 	Width. Not to exceed 10 feet 0 inches.

b. 	Length. Overall combination length must comply with Iowa Code section 321.457.

c. 	Height. Statutory: Not to exceed 13 feet 6 inches.

d. 	Weight. See rule 761—511.14(321,321E).

e. 	Speed. Rescinded IAB 2/7/01, effective 3/14/01.

f. 	Roadway width. At least 24 feet 0 inches.

g. 	Limited movement. Movement shall be solely for the purpose of delivery or transfer from the point of manufacture or assembly to another point of manufacture or assembly within the state or to a point outside the state and shall be on the most direct route necessary for the movement.

511.9(6) Vehicles with divisible loads of hay, straw, stover, or bagged livestock bedding provided the following are not exceeded:

a. 	Width. 12 feet 5 inches.

b. 	Length. Statutory: 75 feet.

c. 	Height. Statutory: 14 feet 6 inches.

d. 	Weight. See rule 761—511.14(321,321E).

e. 	Distance. Movement is allowed for unlimited distance; routing through the vehicle and motor carrier services bureau and city and county jurisdictions is not required.

511.9(7) Necessary trip routes must be obtained from the appropriate city and county jurisdictions.

This rule is intended to implement Iowa Code sections 321.454, 321.456, 321.457, 321.463, 321E.2, 321E.3, 321E.8, 321E.10 and 321E.29.

[ARC 3193C, IAB 7/5/17, effective 8/9/17; ARC 4985C, IAB 3/11/20, effective 4/15/20]