567—81.4 (455B) Water treatment plant grades.

81.4(1) Classifications. The water treatment plant classifications are listed in the following table:

Water Treatment Plant Classifications

| Treatment Type | Grade* |
| --- | --- |
|  | Average Daily Pumpage in MGD |
|  | 0-0.1 | >0.1-0.5 | >0.5-1.5 | >1.5 |
| 1. Iron or manganese removal; aeration; chlorination; fluoridation; stabilization; any other chemical addition; or any combination of these processes | I | II | II | III |
| 2. Ion exchange | II | II | III | III |
| 3. Direct surface water filtration | II | II | III | III |
| 4. Utilization of lime, soda ash or other chemical addition for pH adjustment in the precipitation and coagulation of iron or manganese | II | II | III | III |
| 5. Complete surface water clarification or lime softening of surface water or groundwater | III | III | III | IV |
| 6. Reverse osmosis and electrodialysis | II | II | III | IV |
| 7. Activated carbon for THM or synthetic organics removal | III | III | III | IV |

*For Grade A water supply classification, see subrule 81.6(1).

81.4(2) Average daily pumpage. When the average daily pumpage is unknown, the plant grade will be determined from the population of the most recent census and an evaluation of commercial, industrial, and other users.