199—9.8(479,479B) Notice of violation and halting construction.

9.8(1) Notice of violation. If the county inspector identifies a violation of the standards adopted in this chapter, Iowa Code section 479.29 or 479B.20, or a separate agreement between the pipeline company and the landowner, the county inspector shall give verbal notice, followed by written notice, to the pipeline company and the pipeline company’s contractor and require the pipeline company to take corrective action.

9.8(2) Halting construction. A county inspector may temporarily halt construction at the location of the dispute if construction is not in compliance with the standards adopted in this chapter, the land restoration plan, or the terms of an independent agreement between the pipeline company and landowner regarding land restoration or line location until the county inspector consults with a supervisor of the pipeline company or contractor. If, after consultation with a supervisor of the pipeline company or contractor, agreement on corrective action to address the violation cannot be reached, the county inspector may submit a request to the county board of supervisors for resolution of the issue. Construction may not resume at the disputed location either (1) until the county inspector and supervisor of the pipeline company reach an agreement on a resolution or (2) where the board of supervisors has been contacted, until the board of supervisors has responded or after one business day after contact by the county inspector. If a resolution is not reached, construction may continue; however, the pipeline company will be responsible for any damages or for correcting any violation.

[ARC 5685C, IAB 6/16/21, effective 7/21/21]