567—9.5(455B) Criteria for permitting authority at rural water systems.  The requirements for permitting authority at rural water systems incorporated under Iowa Code chapter 357A or 504 are as follows:

9.5(1) Permitting authority under this rule applies only to extensions which:

a. 	Primarily serve residential consumers and will not result in an increase greater than 5 percent of the capacity of the treatment works or system, or will serve fewer than 250 dwelling units.

b. 	In the case of sewer extensions, will not exceed the capacity of any treatment works which received a federal or state monetary grant after 1972.

c. 	In the case of water main extensions, will not exceed the production capacity of any system constructed after 1972.

9.5(2) The rural water system’s standard specifications must be in conformance with the Iowa Standards for Sewer Systems cited in 567—paragraph 64.2(9)“b,” or the water supply construction standards in 567—43.3(455B), and must be filed with and approved by the department. The system’s hydraulic modeling must comply with the water supply distribution system standards pursuant to rule 567—43.3(455B).

9.5(3) The reviewing engineer shall be licensed as a professional engineer in Iowa and shall be employed or retained by the rural water system.

9.5(4) When reviewing applications for sewer and water supply distribution system extensions under its jurisdiction, the rural water system shall use the Iowa Standards for Sewer Systems, the water supply construction standards in rule 567—43.3(455B), and the local standard specifications approved by the department.

9.5(5) The rural water system shall use Form 542-1003 or Form 542-1058, as applicable, when reviewing plans. Upon issuance of each permit, the rural water system shall submit to the department a copy of the permit and a copy of the form used during the review.

9.5(6) The rural water system shall submit to the department a complete quarterly report using Form 542-1005 by the fifteenth day of the month following each quarter of the calendar year.

9.5(7) Plans for which a construction permit has been issued shall be retained on file by the rural water system for the life of the extension.

[ARC 5052C, IAB 6/17/20, effective 7/22/20]