761—720.15 (328) Airport closing.

720.15(1) Notice. When an airport ceases operation for any reason, the sponsor shall notify the department, return the registration certificate and mark the landing area to clearly indicate that the airport is closed to air traffic.

720.15(2) Marking. All marking indicating a usable runway shall be obliterated. The sponsor shall place at a central location a yellow X in accordance with FAA Advisory Circular 150/5340-1J as amended through April 29, 2005.

720.15(3) Temporary closing. When conditions require the temporary closing of a runway, it shall be marked on both ends with a yellow X in accordance with FAA Advisory Circular 150/5340-1J as amended through April 29, 2005.