761—511.15(321,321E) Annual fluid milk products permits. Annual permits are issued for indivisible loads of fluid milk products for travel when the weight of the vehicle or load exceeds statutory limits. Routing is subject to embargoed bridges and roads and posted speed limits. The owner or operator shall select a route using the vertical clearance map and road construction and travel restrictions map provided by the department. Route, detour, road embargo and bridge embargo for fluid milk products information may be found online at www.511ia.org and the department’s website.

511.15(1) The following shall not be exceeded:

a. 	Width. Statutory: 8 feet 6 inches including appurtenances.

b. 	Length. Statutory: 75 feet 0 inches overall.

c. 	Height. Statutory: 13 feet 6 inches.

d. 	Weight. See rule 761—511.16(321,321E).

e. 	Distance. Movement is allowed for unlimited distance on the primary road system, including the interstate, provided the vehicle is transporting fluid milk products to or from a milk plant, receiving station, or transfer station; routing through the motor vehicle division is not required.

511.15(2) Reserved.

This rule is intended to implement Iowa Code sections 321.454, 321.456, 321.457, 321.463, 321E.2, 321E.3, 321E.8, 321E.10 and 321E.29A.

[ARC 6405C, IAB 7/13/22, effective 8/17/22]