567—38.8 (455B) Permit issuance and conditions.

38.8(1) When issued. Upon receipt of a complete application, the department or contracting county shall issue a permit to the landowner or landowner’s agent except as provided in rule 38.12(455B).

38.8(2) Not a water withdrawal permit. Each permit shall include notification that a private well construction permit is not a water withdrawal permit and does not eliminate the necessity of obtaining any water withdrawal permits required in 567—Chapters 50 through 54. A water withdrawal permit is required before an applicant can withdraw more than 25,000 gallons of water per day from any source or combination of sources in the state of Iowa.

38.8(3) Construction by certified well contractor. Each well construction permit shall require that each well be constructed by a certified well contractor in compliance with 567—Chapters 49 and 82. However, temporary dewatering wells at construction sites shall be exempt from the construction standards of 567—Chapter 49.