567—71.1(455B) Bridges, culverts, temporary stream crossings, and road embankments. Approval by the department for the construction, operation, and maintenance of bridges, culverts, temporary stream crossings, and road embankments shall be required in the following instances.

71.1(1) Rural area—floodway. In rural areas, bridges, culverts, road embankments, and temporary stream crossings in or on the floodway of any river or stream draining more than 100 square miles. (Note: Channel modifications associated with bridge, culvert or roadway projects may need approval; see 567—71.2(455B).)

71.1(2) Rural area—floodway and floodplain. Road embankments located in the floodway or floodplains, but not crossing the channel of a river or stream draining more than 10 square miles, where such works occupy more than 3 percent of the cross-sectional area of the channel at bankfull stage or where such works obstruct more than 15 percent of the total cross-sectional area of the floodplain at any stage. In determining a 15 percent occupancy of the floodplain, the concept of equal and opposite conveyance as defined in 567—Chapter 70 shall apply.

71.1(3) Urban areas. In urban areas, bridges, culverts, road embankments and temporary stream crossings in or on the floodway or floodplains of any river or stream draining more than 2 square miles.