875—76.7 (89A) Alterations. When any combination of alterations or changes is made constituting more than 50 percent of the elevator construction, the entire elevator shall be brought into compliance with ASME A17.1-2004, A17.1a-2005 and A17.1S-2005 and shall be deemed a new elevator. Alterations or changes constitute more than 50 percent of the construction if they exceed 50 percent of the total points according to the following table:

| Elevator Component | Hydraulic | Traction |
| --- | --- | --- |
| Controller | 31 | 26 |
| Floor selector | 4 | 8 |
| Drive-MG-SCR | - | 13 |
| Main machine | - | 15 |
| Machine motor | 5 | 7 |
| Hoist ropes | 4 | 8 |
| Governor | 4 | 7 |
| Platform | 9 | 9 |
| Car fixtures | 9 | 8 |
| Cab | 10 | 10 |
| Safeties | 6 | 7 |
| Door operator | 12 | 12 |
| Hoistway door panels | 11 | 10 |
| Hoistway door frames | 11 | 10 |
| Hoistway hangers & tracks | 11 | 11 |
| Hoistway door locks | 8 | 9 |
| Traveling cable | 6 | 9 |
| Hoistway wiring | 8 | 6 |
| Hall fixtures | 8 | 10 |
| Buffers | 6 | 6 |
| Counterweight | 4 | 7 |
| Rails & brackets | 10 | 18 |
| Car & cwt. guides | 6 | 6 |
| Pump | 9 | - |
| Valve | 9 | - |
| Tank | 9 | - |
| Plunger | 14 | - |
| Cylinder | 18 | - |
| Total Points | 242 | 233 |

If any of the above elevator components do not apply, the points for the component(s) shall be subtracted from the total points before a determination of whether the alteration or change constitutes 50 percent is made.