321—25.40 (231C) Structural requirements.

25.40(1) General requirements.

a.   	 The structure of the program shall be designed and operated to meet the needs of the tenants.

b.   	 The buildings and grounds shall be well-maintained, clean, safe and sanitary.

c.   	 Programs shall have private dwelling units with a single-action lockable entrance door.

d.   	 A program serving persons with cognitive impairment or dementia, whether in a general or dementia-specific setting, shall have the means to disable or remove the lock on an entrance door, and shall do so if the presence of the lock presents a danger to the health and safety of the tenant.

e.   	 The structure in which a program is housed shall be built at a minimum of Type V (111) construction as given in Section 22.3.1.3.3 and Sections 6.2.1A to 6.2.2 of NFPA 101, Life Safety Code, 1994 edition, published by the National Fire Protection Association, 1 Batterymarch Park, Quincy, Massachusetts 02169-7471, or as required in administrative rules promulgated by the state fire marshal.

f.   	 Programs may have individual cooking facilities within the private dwelling units. Any program serving persons with cognitive impairment or dementia, whether in a general or dementia-specific setting, shall have the means to disable or easily remove appliances, and shall do so if the presence of cooking appliances presents a danger to the health and safety of the tenant or others.

25.40(2) Programs certified prior to July 4, 2001. Facilities for programs certified prior to July 4, 2001, shall meet the following requirements:

a.   	 Each dwelling unit shall have at least one room that shall have not less than 120 square feet of floor area. Other habitable rooms shall have an area of not less than 70 square feet.

b.   	 Each dwelling unit shall have not less than 190 square feet of floor area, excluding bathrooms.

c.   	 A dwelling unit used for double occupancy shall have not less than 290 square feet of floor area, excluding bathrooms.

d.   	 The program shall have a minimum common area of 15 square feet per tenant.

25.40(3) New construction built on or after July 4, 2001. Programs operated in new construction built on or after July 4, 2001, shall meet the following requirements:

a.   	 Each dwelling unit shall have at least one room that shall have not less than 120 square feet of floor area. Other habitable rooms shall have an area of not less than 70 square feet.

b.   	 Each dwelling unit used for single occupancy shall have a total square footage of not less than 240 square feet of floor area, excluding bathrooms and door swing.

c.   	 A dwelling unit used for double occupancy shall have a total square footage of not less than 340 square feet of floor area, excluding bathrooms and door swing.

d.   	 Each dwelling unit shall contain a bathroom, including but not limited to a toilet, sink and bathing facilities. A program serving persons with cognitive impairment or dementia, whether in a general or dementia-specific setting, shall have the means to disable or remove the sink or bathing facility water control, and shall do so if the presence of the water control presents a danger to the health and safety of the tenant.

e.   	 The program shall have a minimum of 25 square feet of common space per tenant.

25.40(4) Structure being converted to or rehabilitated for use for a program on or after July 4, 2001. A program operating in a structure that was converted or rehabilitated for use for a program on or after July 4, 2001, shall meet the following requirements:

a.   	 Each dwelling unit shall have at least one room that has not less than 120 square feet of floor area. Other habitable rooms shall have an area of not less than 70 square feet.

b.   	 Each dwelling unit used for single occupancy shall have a total square footage of not less than 190 square feet of floor area, excluding bathrooms and door swing.

c.   	 A dwelling unit used for double occupancy shall have a total square footage of not less than 290 square feet of floor area, excluding bathrooms and door swing.

d.   	 The program shall have a minimum common area of 15 square feet per tenant dedicated for use by the program tenants.

e.   	 Each dwelling unit shall have a bathroom, including but not limited to a toilet, sink and bathing facilities.

f.   	 Each sleeping room shall have a minimum of 5.7 square feet of operable window. Waiver of this requirement may be granted by the state fire marshal or designee.