491—12.15 (99F) Computer recording requirements and monitoring of slot machines.

12.15(1) A facility shall have a computer connected to each slot machine in the casino to record and monitor the slot machine’s activities.

12.15(2) The computer shall be designed and operated to automatically perform the functions relating to slot machine meters in the casino as follows:

a.   	 Record the number and total of moneys placed in the slot machine for the purpose of activating play.

b.   	 Record the number and total of moneys in the container(s).

c.   	 Record the number and total of moneys to be paid manually as the result of a jackpot.

d.   	 Record the electronic meter information required by 491—subrule 11.10(4).

12.15(3) The computer shall monitor and detect machine exception codes and error messages as required by 491—subrule 11.10(5) and 491—11.11(99F).

12.15(4) The computer shall store in machine-readable form all information required by subrules 12.15(2) and 12.15(3) and the stored data shall not be susceptible to change or removal.

12.15(5) The licensee shall maintain a current log, accessible to commission representatives, of all changes and updates made to the computer system. All changes and updates shall be approved as required by 491—subrule 11.4(1).