761—119.2 (321) General.

119.2(1) Conformance to MUTCD. Tourist-oriented directional signing shall conform to the “Manual on Uniform Traffic Control Devices” (MUTCD), as adopted in rule 761—130.1(321).

119.2(2) Spacing and location.

a.    	 Tourist-oriented directional signing shall be installed only when sufficient space is available.

b.    	 Tourist-oriented directional signing shall be installed in advance of the intersection where the motorist leaves the primary highway system to travel to the activity or site. However, tourist-oriented directional signs may be placed on a higher classified highway to direct motorists onto a lower classified highway, or on a greater traveled highway to direct motorists onto a lesser traveled highway.

c.    	 Tourist-oriented directional signing shall not be placed at interchanges. If an at-grade intersection on a primary highway is replaced with an interchange, the intersection will no longer qualify for tourist-oriented directional signing. Any tourist-oriented directional signing previously erected shall be removed by the department.

d.    	 If an adjacent landowner complains to the department about the placement of a tourist-oriented directional sign, the department shall attempt to reach an agreement with the landowner for relocating the sign. If possible, the sign shall be relocated to the least objectionable place.

e.    	 Tourist-oriented directional signing shall not be placed within the urban area as established by the U.S. Census Bureau of an incorporated municipality with a population of 5000 or more.

119.2(3) Advance signing. Advance signing authorized by the MUTCD may be installed where the department determines that advance notification of an activity or site would reduce vehicle conflicts and improve highway safety.

119.2(4) Message. The message on a tourist-oriented directional sign is limited to a descriptive name, a directional arrow, and travel distance to the activity or site. However, if an agricultural business activity offers tours, the message for the activity shall include the word “tours.”

[ARC 1202C, IAB 12/11/13, effective 1/15/14]