HF 2375 (LSB 5428HV (4) 84)

HOUSE FILE 2375

BY  COMMITTEE ON COMMERCE

(SUCCESSOR TO HSB 558)

A BILL FOR

An Act specifying procedures applicable to claims asserting stray electric current or voltage.

BE IT ENACTED BY THE GENERAL ASSEMBLY OF THE STATE OF IOWA:

Section 1.  NEW SECTION.  476D.1  Short title.

This chapter shall be known and may be cited as the “Stray Current and Voltage Remediation Act”.

Sec. 2.  NEW SECTION.  476D.2  Definitions.

As used in this chapter, unless the context otherwise requires:

1.  “Board”means the utilities board within the utilities division of the department of commerce.

2.  “Cow contact points” means any two electrically conductive points which a dairy cow may, in its normal environment, unavoidably and simultaneously contact.

3.  “Dairy producer” means any person or entity that owns or operates a dairy farm or that owns cows that do or are intended to produce milk.

4.  “Preventive action level” is stray current or voltage constituting either of the following:

a.  A steady-state, root mean square alternating current of two milliamp or more through a five hundred ohm resistor connected between cow contact points, as measured by a true root mean square meter.

b.  A steady-state, root mean square alternating current voltage of one volt or more, across or in parallel with a five hundred ohm resistor connected between cow contact points, as measured by a true root mean square meter.

5.  “Steady-state” means the value of a current or voltage after an amount of time where all transients have decayed to a negligible value.

6.  “Stray current or voltage” means either of the following:

a.  Any steady-state, sixty hertz, including harmonics thereof, root mean square alternating current of less than twenty milliamp through a five hundred ohm resistor connected between cow contact points, as measured by a true root mean square meter.

b.  Any steady-state, sixty hertz, including harmonics thereof, root mean square alternating current voltage of less than ten volts, across or in parallel with a five hundred ohm resistor connected between cow contact points, as measured by a true root mean square meter.

7.  “Utility” means a public utility as defined in Code section 476.1, or for purposes of this chapter, any other person owning or operating more than one thousand five hundred miles of transmission lines and associated facilities in this state.

Sec. 3.  NEW SECTION.  476D.3  Rules —— scope of authority.

1.  The board shall by rule establish standard procedures and protocols which may be used for the measurement of stray current or voltage. The board shall review the rules from time to time, or upon petition to the board, to ensure that the standard procedures and protocols continue to be scientifically and technologically accurate and a reliable means of detecting stray current or voltage. Other measurements of stray current or voltage made using other procedures and protocols may be considered by the board in appropriate cases.

2.  The purpose for the standard procedures and protocols established by rule pursuant to subsection 1 shall be for utilization by a utility in taking measurements of stray current or voltage, and by the board in preparing a determination of source document that may be utilized by either a dairy producer or a utility as evidence of the source and level, if any, of stray current or voltage. The determination of source document shall be based on qualified, measurable, scientific facts. Neither the board, nor the determination of source document, shall establish liability or civil damages in connection with a civil lawsuit.

Sec. 4.  NEW SECTION.  476D.4  Stray current or voltage program —— claims —— notice —— utility response.

1.  A dairy producer in this state that claims that its dairy cows are being affected by stray current or voltage may participate in the stray voltage program. The dairy producer shall provide written notice to the utility and may provide notice to the board to participate in the program. The notice shall include a nonbinding statement as to why the dairy producer claims its dairy cows are being affected by electrical energy attributable to the utility.

2.

a.  Within fourteen business days after receipt of a notice alleging stray current or voltage by a utility pursuant to subsection 1, the utility shall take or arrange for the taking of measurements to identify the existence and magnitude of the stray current or voltage, if any. A dairy producer providing notice of the claim shall permit entry onto the dairy farm at dates and times mutually agreed upon by the dairy producer and the utility. The utility shall perform no other service or inspection on the dairy farm beyond taking measurements of stray current or voltage, except the utility may advise the dairy producer as to recommended on-farm remedial action and may perform such remedial action with the permission of the dairy producer. The utility or its representative shall abide by the dairy farm’s biosecurity protocols or, if none, generally accepted biosecurity protocols in the industry, prior to entry onto the dairy farm. The utility shall be provided advance notice of any biosecurity protocols adopted by the dairy producer.

b.  A dairy producer may include with the notice provided pursuant to subsection 1, or in a subsequent notice, a written request for the board to take or arrange for the taking of separate and independent measurements to identify the existence and magnitude of stray current or voltage, if any. Such a request may also be made by the utility. Measurements by the board shall be taken by a representative of the board directly, or by a neutral third-party expert selected by the board for such purposes. The board or a selected third-party expert shall perform no other service or inspection on the dairy farm beyond taking measurements of stray current or voltage, except the board or third-party expert may advise the dairy producer as to recommended on-farm remedial action. The board or the third-party expert shall abide by the dairy farm’s biosecurity protocols or, if none, by generally accepted biosecurity protocols in the industry, prior to entry onto the dairy farm. The board shall subsequently prepare or cause to be prepared the determination of source document as described in section 476D.3 which shall be made available to both the dairy producer and the utility.

3.  If the utility or the board’s measurements identify a level of stray current or voltage at cow contact points in excess of the preventive action level, the utility or the board, as applicable, shall promptly identify if the utility’s distribution system’s contribution is greater than one milliamp or one volt, measured in the same manner as the preventive action level. For purposes of this determination, stray current or voltage on the utility’s distribution system shall be attributed to the utility even if caused by other customers connected to the utility’s distribution system. If that portion of the stray current or voltage at cow contact points attributable to the utility’s distribution system exceeds one milliamp or one volt, the utility shall, within fifteen business days, commence and diligently pursue to completion, remedial procedures which result in, and are reasonably likely to sustain, a reduction of the stray current or voltage at cow contact points attributable to the utility’s distribution system to one milliamp or less or one volt or less, measured in accordance with the rules established by the board.

Sec. 5.  NEW SECTION.  476D.5  Civil actions.

A civil action shall not be commenced by a dairy producer against a utility seeking damages or other relief allegedly due to injury caused by stray current or voltage unless the dairy producer has provided notice of its participation in the stray current or voltage program in accordance with section 476D.4 at least ninety days prior to filing such an action. In any civil action against a utility for damages or other relief, the written documentation prepared by or on behalf of the board pursuant to section 476D.4 may be admissible in evidence. Any and all civil damages shall be determined by a court of law, and shall be based on evidence provided by both parties.

EXPLANATION

This bill specifies procedures applicable to claims asserting stray electric current or voltage impacting dairy cows.

The bill provides for the adoption of administrative rules by the Iowa utilities board establishing standard procedures and protocols for the measurement of stray current or voltage. The bill directs the board to review the rules periodically to ensure that they remain accurate and reliable with regard to stray current or voltage measurement, and provides that other forms of measurement may be considered by the board in appropriate cases. The bill states that the purpose for the standard procedures and protocols shall be for utilization by a utility in taking measurements of stray current or voltage, and by the board in preparing a determination of source document that may be utilized by either a dairy producer or a utility as evidence of the source and level, if any, of stray current or voltage. The bill provides that the determination of source document shall be based on qualified, measureable, scientific facts, and that neither the board, nor the document, shall establish liability or civil damages in connection with a civil lawsuit.

The bill provides that a dairy producer in Iowa who claims that its dairy cows are being affected by stray current or voltage may participate in a stray voltage program by providing written notice to the utility and, optionally, to the board containing a nonbinding statement as to why the dairy producer believes its dairy cows are being affected by electrical energy attributable to the utility.

Within 14 business days after receipt of the notice, the bill requires the utility to take or arrange for the taking of measurements to identify the existence and magnitude of the stray current or voltage, if any. The bill prohibits the utility from performing any other service or inspection on the dairy farm beyond taking the measurements other than advising the dairy producer as to recommended on-farm remedial action and performing such remedial action with permission. The bill provides that the utility or its representative shall abide by the dairy farm’s biosecurity protocols, or if none, generally accepted biosecurity protocols in the industry prior to entry onto the dairy farm, and requires the dairy producer to provide advance notice of any biosecurity protocols they have adopted to the utility.

The bill provides that a dairy producer, or a utility, may request that the board take or arrange for the taking of separate and independent measurements to identity the existence and magnitude of stray current or voltage, if any, either directly or by a neutral third-party expert selected by the board for such purposes. The bill applies the same restrictions regarding performing no other service or inspection and abiding by biosecurity protocols as are applicable to measurements taken by the utility. After measurements are taken by or on behalf of the board, the board must prepare or cause to be prepared the determination of source document and make the document available to both the dairy producer and the utility.

The bill states that if the utility or the board’s measurements identify a level of stray current or voltage at cow contact points in excess of the preventive action level, as defined in the bill, the utility or the board, as applicable, shall promptly identify if the utility’s distribution system’s contribution is greater than one milliamp or one volt. For purposes of this determination, the bill provides that stray current or voltage on the utility’s distribution system shall be attributed to the utility even if caused by other customers connected to the utility’s distribution system. If that portion of the stray current or voltage at cow contact points attributable to the utility’s distribution system exceeds one milliamp or one volt, the bill directs the utility to within 15 business days commence and diligently pursue to completion remedial procedures which result in, and are reasonably likely to sustain, a reduction of the stray current or voltage to one milliamp or less or one volt or less, measured in accordance with the rules established by the board.

The bill provides that a civil action shall not be commenced by a dairy producer against a utility seeking damages or other relief allegedly due to injury caused by stray current or voltage unless the dairy producer has provided notice of its participation in the stray current or voltage program at least 90 days prior to filing the action. The bill states that in such an action the written documentation prepared by or on behalf of the board may be admissible in evidence, but that any and all civil damages shall be determined by a court of law based on evidence provided by both parties.