HOUSE FILE _____

BY  (PROPOSED COMMITTEE ON COMMERCE BILL BY CHAIRPERSON SODERBERG)

A BILL FOR

An Act relating to stray electric current or voltage and civil actions to recover resulting damages.

BE IT ENACTED BY THE GENERAL ASSEMBLY OF THE STATE OF IOWA:

Section 1.  NEW SECTION.  476D.1  Short title.

This chapter shall be known and may be cited as the “Stray Current and Voltage Remediation Act”.

Sec. 2.  NEW SECTION.  476D.2  Legislative findings and intent.

The general assembly finds that the efficient and safe distribution of electricity is critical to the well-being of the citizens and economy of this state, including the business of agriculture, and that this chapter is necessary for the protection of the public welfare. The general assembly recognizes that stray current or voltage is a normal, inherent, and unavoidable result of electricity traveling through grounded electrical systems, including a dairy producer’s on-farm system and a utility’s distribution system, which systems are required by the national electrical code and the national electrical safety code to be grounded to the earth to ensure continuous safety and reliability. The general assembly finds that the potential impact of stray current or voltage on dairy cows is a matter of interest and concern to dairy producers with dairies situated near and served by a multigrounded multiple exchange electrical distribution system or similar electrical distribution system utilized by utilities in this state. Scientific research has established a level of stray current or voltage at or below which no effect on a dairy cow’s behavior, health, or milk production has been shown. To provide for the continued safe and efficient availability of electricity while addressing complaints regarding stray current or voltage, it is necessary and appropriate to establish a uniform preventive action level; establish uniform procedures and protocols for measurements of stray current or voltage; require, when necessary, that the sources of stray current or voltage be identified; require, when necessary, adequate remediation; and establish procedures for handling complaints.

Sec. 3.  NEW SECTION.  476D.3  Definitions.

As used in this chapter, unless the context otherwise requires:

1.  “Adequate remediation” means corrective action by a utility which results in, and is reasonably likely to sustain, a reduction of stray current or voltage attributable to the utility’s distribution system to fifty percent or less of the preventive action level.

2.  “Board”means the utilities board within the utilities division of the department of commerce.

3.  “Cow contact points” means any two electrically conductive points which a dairy cow may, in its normal environment, unavoidably and simultaneously contact.

4.  “Dairy producer” means any person or entity that owns or operates a dairy farm or who owns cows that do or are intended to produce milk.

5.  “Preventive action level” is stray current or voltage constituting either of the following:

a.  A steady-state, root mean square alternating current of two milliamp or more through a five hundred ohm resistor connected between cow contact points, as measured by a true root mean square meter.

b.  A steady-state, root mean square alternating current voltage of one volt or more, across or in parallel with a five hundred ohm resistor connected between cow contact points, as measured by a true root mean square meter.

6.  “Steady-state” means the value of a current or voltage after an amount of time where all transients have decayed to a negligible value.

7.  “Stray current or voltage” means either of the following:

a.  Any steady-state, sixty hertz, including harmonics thereof, root mean square alternating current of less than twenty milliamp through a five hundred ohm resistor connected between cow contact points, as measured by a true root mean square meter.

b.  Any steady-state, sixty hertz, including harmonics thereof, root mean square alternating current voltage of less than ten volts, across or in parallel with a five hundred ohm resistor connected between cow contact points, as measured by a true root mean square meter.

8.  “Utility” means a public utility as defined in Code section 476.1.

Sec. 4.  NEW SECTION.  476D.4  Rules.

The board shall by rule establish standard procedures and protocols which may be used for the measurement of stray current or voltage. The board shall review the rules from time to time, or upon petition to the board, to ensure that the standard procedures and protocols continue to be scientifically and technologically accurate and a reliable means of detecting stray current or voltage. Other measurements of stray current or voltage made using other procedures and protocols may be considered by the board in appropriate cases.

Sec. 5.  NEW SECTION.  476D.5  Claims —— notice —— utility response.

1.  A dairy producer in this state who claims that its dairy cows are being affected by any form or type of electrical energy allegedly attributable to a utility including, without limitation, stray current or voltage, shall, before commencing any civil action against the utility, provide written notice of the claim to the utility. The notice shall specify why the dairy producer believes its dairy cows are being affected by electrical energy attributable to the utility. Within fourteen business days of receipt of such notice, if the notice alleges stray current or voltage, the utility shall make arrangements to take or cause measurements to be taken at cow contact points at the dairy producer’s dairy to identify the existence and magnitude of stray current or voltage, if any.

2.  If the utility finds a level of stray current or voltage at cow contact points in excess of the preventive action level, the utility shall promptly identify that portion, if any, of the stray current or voltage that is attributable to the utility’s distribution system. If that portion of the stray current or voltage at cow contact points attributable to the utility’s distribution system exceeds fifty percent of the preventive action level, the utility shall, within fifteen business days, commence and diligently pursue to completion, remedial procedures which result in, and are reasonably likely to sustain, a reduction of the stray current or voltage at cow contact points attributable to the utility’s distribution system to fifty percent or less of the preventive action level.

Sec. 6.  NEW SECTION.  476D.6  Jurisdiction —— contested case proceedings —— orders.

The board shall have exclusive, initial jurisdiction regarding actions taken pursuant to section 476D.5. Upon receiving a request from a dairy producer to review such actions, the board shall conduct a contested case proceeding pursuant to chapter 17A to determine whether a utility has complied with the board’s rules regarding measurement of stray current or voltage, whether the utility’s measurements demonstrated stray current or voltage at or above the preventive action level, whether any other measurements demonstrated stray current or voltage at or above the preventive action level, whether the utility properly identified that portion of the stray current or voltage at cow contact points attributable to the utility’s distribution system, and whether the utility has complied with its remediation obligation under this chapter. The board may also arrange for third-party measurement of stray current or voltage in cases in which the board finds it reasonable to do so.

1.  If the board determines that the utility complied with the rules regarding measurement of stray current or voltage, and properly identified no stray current or voltage in excess of the preventive action level, the board may issue an order that the utility has provided adequate service. The board’s order shall be binding on the parties.

2.  If the board determines that the utility complied with the rules regarding measurement of stray current or voltage, the utility properly identified stray current or voltage in excess of the preventive action level, and the utility properly identified that the portion of stray current or voltage attributable to the utility’s distribution system was fifty percent or less of the preventive action level, the board may issue an order that the utility provided adequate service. The board’s order shall be binding on the parties, subject only to the provisions of section 476D.7.

3.  If the board determines that the utility complied with the rules regarding measurement of stray current or voltage, the utility properly identified stray current or voltage in excess of the preventive action level, and the utility properly identified that the portion of stray current or voltage attributable to the utility’s distribution system exceeded fifty percent of the preventive action level, the board may determine the adequacy of the utility’s remediation efforts. The board’s order shall be binding on the parties, subject only to the provisions of section 476D.7. If the dairy producer has complied with the notice provisions set forth in section 476D.5, and the board has made a determination that the conditions set forth in this subsection are met, then the dairy producer may, not later than one year following completion of adequate remediation, or one year following the issuance of the board’s final order, whichever occurs later, commence a civil action seeking monetary damages against the utility. In any such civil action, damages shall be limited as set forth in section 476D.8.

4.  If the board determines that the utility failed to comply with the rules regarding measurement of stray current or voltage, the utility failed to properly identify, when required pursuant to section 476D.5 to do so, that portion of stray current or voltage attributable to the utility’s distribution system, or the utility failed to provide adequate remediation, the board shall order the utility to take measurements of stray current or voltage in conformance with board rules, or identify that portion of the stray current or voltage attributable to the utility’s distribution system and, if necessary, to provide adequate remediation. The board’s order shall be binding on the parties, subject only to the provisions of section 476D.7. If the dairy producer complied with the notice provisions set forth in section 476D.5, and the board made a determination that the portion of stray current or voltage attributable to the utility’s distribution system exceeded fifty percent of the preventive action level, then the dairy producer may, not later than one year following completion of adequate remediation, or one year following the issuance of the board’s final order, whichever occurs later, commence a civil action seeking monetary damages against the utility. In any such civil action, damages shall be limited as set forth in section 476D.8.

5.  If the board determines that a dairy producer made or pursued a claim in bad faith or for purposes of harassment of the utility, the board shall require the dairy producer to pay the utility’s actual costs of investigation and defense. If the board determines that a utility acted in bad faith, or for purposes of harassment or delay, the board shall require the utility to pay the dairy producer’s actual costs of investigation, if any, and costs of preparation and presentation of the claim before the board. The board’s order shall be binding on the parties, subject only to the provisions of section 476D.7.

Sec. 7.  NEW SECTION.  476D.7  Civil actions.

A civil action shall not be commenced by a dairy producer against a utility seeking damages or other relief allegedly due to injury caused by any form or type of electrical energy allegedly attributable to a utility including, without limitation, stray current or voltage unless the dairy producer has complied with the provisions of section 476D.5, and the board has issued an order pursuant to section 476D.6. In any civil action against a utility for damages or other relief, after the dairy producer has complied with the provisions of section 476D.5, and the board has issued an order pursuant to section 476D.6, the board’s order shall be admissible in evidence in such civil action.

Sec. 8.  NEW SECTION.  476D.8  Damages.

In any civil action against a utility for damages pursuant to this chapter or other causes of action where damages are alleged to be caused by any form or type of electrical energy allegedly attributable to a utility including, without limitation, stray current or voltage, a dairy producer shall be limited to those damages which were incurred by the dairy producer during that period of time commencing twelve months prior to the dairy producer’s provision of notice to the utility and ending on the date of completion of adequate remediation, if any, and with respect to stray current or voltage claims, were caused by that portion of the stray current or voltage attributable to the utility’s distribution system. In any action for damages, a utility may assert a defense of comparative fault as set out in section 668.3.

Sec. 9.  Section 657.1, subsection 2, Code 2011, is amended to read as follows:

2.  Notwithstanding subsection 1, in an

any type of nuisance action to abate a nuisance against an electric utility, an electric utility may assert a defense of comparative fault as set out in section 668.3 if the electric utility demonstrates that in the course of providing electric services to its customers it has complied with engineering and safety standards as adopted by the utilities board of the department of commerce, and if the electric utility has secured all permits and approvals, as required by state law and local ordinances, necessary to perform activities alleged to constitute a nuisance.

In addition, a claim for nuisance shall not be asserted against an electric utility for damages due to stray current or voltage. Any claim against an electric utility for damages due to stray current or voltage shall be limited to claims of negligence, and shall be subject to the provisions of chapters 476D and 668. The utility’s conduct in such claims shall be judged using a standard of ordinary care under the existing circumstances.

EXPLANATION

This bill concerns stray electric current or voltage, including the potential impact of stray electric current or voltage on dairy cows, and specifies procedures for adopting rules, filing complaints, measuring stray electric current or voltage, taking corrective action, and pursuing civil actions for damages.

The bill commences with a statement of legislative intent, noting that the general assembly finds that the potential impact of stray current or voltage on dairy cows is a matter of interest and concern to dairy producers with dairies situated near and served by electrical distribution systems utilized by utilities in Iowa, and that scientific research has established a level of stray current or voltage at or below which no effect on a dairy cow’s behavior, health, or milk production has been shown.

The bill provides for the adoption of administrative rules by the Iowa utilities board establishing standard procedures and protocols for the measurement of stray current or voltage. The bill states that other measurements of stray current or voltage made using other procedures and protocols may be considered by the board in appropriate cases.

The bill provides that a dairy producer who claims that its dairy cows are being affected by any form or type of electrical energy allegedly attributable to a utility including, without limitation, stray current or voltage, shall, before commencing any civil action against the utility, provide written notice to the utility specifying why the dairy producer believes its dairy cows are being affected by electrical energy attributable to the utility. Within 14 business days of receipt of the notice, if the notice alleges stray current or voltage, the bill directs the utility to make arrangements to take or cause measurements to be taken at cow contact points at the dairy producer’s dairy to identify the existence and magnitude of stray current or voltage, if any. The bill states that if a level of stray current or voltage in excess of a specified preventive action level is determined, the utility must identify that portion which is attributable to the utility’s distribution system. If the portion of the stray current or voltage at cow contact points attributable to the utility’s distribution system exceeds 50 percent of the preventive action level, the bill requires the utility, within 15 business days, to commence and diligently pursue to completion remedial procedures which shall reduce, and are reasonably likely to sustain, that portion of the stray current or voltage at cow contact points attributable to the utility’s distribution system to 50 percent or less of the preventive action level.

The bill provides that the board shall have exclusive, initial jurisdiction regarding complaints by dairy producers and actions by utilities. Upon receiving a request from a dairy producer to review such actions, the board shall conduct a contested case proceeding to determine whether a utility has complied with the rules regarding measurement of stray current or voltage, whether the utility’s measurements demonstrated stray current or voltage at or above the preventive action level, whether any other measurements demonstrated stray current or voltage at or above the preventive action level, whether the utility has properly identified that portion of the stray current or voltage at cow contact points attributable to the utility’s distribution system, and whether the utility has complied with its remediation obligation. The board is authorized to arrange for third-party measurement of stray current or voltage if the board determines it reasonable to do so.

The bill provides, pursuant to a contested case proceeding, for the issuance of orders by the board. If a utility is found to have complied with the rules regarding measurement of stray current or voltage, and properly identified no stray current or voltage in excess of the preventive action level, the board may issue an order that the utility has provided adequate service. If a utility complied with the rules regarding measurement of stray current or voltage, properly identified stray current or voltage in excess of the preventive action level, and properly identified that the portion of stray current or voltage attributable to the utility’s distribution system was 50 percent or less of the preventive action level, the board may issue an order that the utility provided adequate service. If a utility complied with the rules regarding measurement of stray current or voltage, the utility properly identified stray current or voltage in excess of the preventive action level, and the utility properly identified that the portion of stray current or voltage attributable to the utility’s distribution system exceeded 50 percent of the preventive action level, the board may determine the adequacy of the utility’s remediation efforts. The bill states that in this event, and if a dairy producer has complied with the notice provisions, the dairy producer may, not later than one year following completion of adequate remediation, or one year following the issuance of the board’s final order thereon, whichever occurs later, commence a civil action seeking monetary damages against the utility. If a utility failed to comply with the rules regarding measurement of stray current or voltage, failed to properly identify when required to do so that portion of stray current or voltage attributable to the utility’s distribution system, or failed to provide adequate remediation, the board shall order the utility to take measurements of stray current or voltage in conformance with board rules, or identify that portion of the stray current or voltage attributable to the utility’s distribution system and, if necessary, to provide adequate remediation. The bill states that if a dairy producer complied with the notice provisions, and the board made a determination that the portion of stray current or voltage attributable to the utility’s distribution system exceeded 50 percent of the preventive action level, the dairy producer may, not later than one year following completion of adequate remediation, or one year following the issuance of the board’s final order, whichever occurs later, similarly commence a civil action seeking monetary damages against the utility. The bill states that if a dairy producer made or pursued a claim in bad faith or for purposes of harassment of the utility, the board shall require the dairy producer to pay the utility’s actual costs of investigation and defense, and if a utility acted in bad faith, or for purposes of harassment or delay, the board shall require the utility to pay the dairy producer’s actual costs of investigation, if any, and costs of preparation and presentation of the claim before the board.

The bill specifies that in any civil action against a utility for damages alleged to be caused by any form or type of electrical energy allegedly attributable to a utility including, without limitation, stray current or voltage, a dairy producer shall be limited to those damages which were incurred by the dairy producer during that period of time commencing 12 months prior to the dairy producer’s provision of notice to the utility and ending on the date of completion of adequate remediation, if any, and with respect to stray current or voltage claims, were caused by that portion of the stray current or voltage attributable to the utility’s distribution system. In any action for damages, a utility may assert a defense of comparative fault as set out in Code section 668.3.

Additionally, with respect to abatement of nuisance provisions contained in Code section 657.1, the bill provides that a claim for nuisance shall not be asserted against an electric utility for damages due to stray current or voltage, and shall be limited to claims of negligence and subject to the bill’s provisions for claims regarding dairy cows and the comparative fault provisions of Code chapter 668. The bill states that a utility’s conduct in such claims shall be judged using a standard of ordinary care under the existing circumstances.