HF 2229 (LSB 5162YH (9) 85)

HOUSE FILE 2229

BY  HEATON

A BILL FOR

An Act relating to lighting requirements for towed machinery or equipment, and making penalties applicable.

BE IT ENACTED BY THE GENERAL ASSEMBLY OF THE STATE OF IOWA:

Section 1.  Section 321.423, subsection 2, paragraph h, Code 2014, is amended to read as follows:
   h.  A flashing amber light is permitted on a towing or recovery vehicle, a utility maintenance vehicle, a municipal maintenance vehicle, a highway maintenance vehicle, or a vehicle operated in accordance with subsection 6, paragraph “a”, or section 321.398 or 321.453.

Sec. 2.  Section 321.423, subsection 2, Code 2014, is amended by adding the following new paragraph:
   NEW PARAGRAPH.  k.  A flashing red light is permitted on towed machinery or equipment in accordance with subsection 6, paragraph “b”.

Sec. 3.  Section 321.423, subsection 6, Code 2014, is amended to read as follows:
   6.  Amber flashing light —— flashing red light.
   a.  A farm tractor, farm tractor with towed equipment, self-propelled implement of husbandry, road construction or maintenance vehicle, road grader, or other vehicle principally designed for use off the highway which, when operated on a primary or secondary road, is operated at a speed of thirty-five miles an hour or less, shall be equipped with and display an amber flashing light visible from the rear at any time from sunset to sunrise. If the amber flashing light is obstructed by the towed equipment, the towed equipment shall also be equipped with and display an amber flashing light as required under this subsection. All vehicles specified in this subsection which are manufactured for sale or sold in this state shall be equipped with an amber flashing light in accordance with the standards of the American society of agricultural engineers.
   b.  In addition to the requirements of paragraph “a”, machinery or equipment towed by a farm tractor or other motor vehicle at any time from sunset to sunrise shall display a flashing red light attached at the rearmost position on the towed machinery or equipment and visible from a distance of five hundred feet to the rear.

EXPLANATION

The inclusion of this explanation does not constitute agreement with

the explanation’s substance by the members of the general assembly.

Under current law, a farm tractor with towed equipment is required to be equipped with and display an amber flashing light visible from the rear at any time from sunset to sunrise. If the amber flashing light is obstructed by the towed equipment, the towed equipment must also be equipped with and display an amber flashing light. In addition to those current requirements, this bill requires that machinery or equipment towed by a farm tractor or other motor vehicle at any time from sunset to sunrise must display a flashing red light visible from 500 feet to the rear. The flashing red light must be attached at the rearmost position on the towed machinery or equipment.

A violation of vehicle lighting requirements is punishable by a scheduled fine of $30.